## Slide 1: App-controlled LEGO robotic arm
Benjamin Schaefer, Christoph Ulrich
HTWG Konstanz, Ubiquitous Computing Lab
Mobile Computing WS2018/19
URL: http://uc-lab.in.htwg-konstanz.de
Notes: Why – how – what
Happy evening everybody, Ulli and I would like to introduce our project "App-controlled LEGO robotic arm" today.

## Slide 2
Motivation
Construction
Kinematics
Application
State of the Art
Demo
Notes: For this, we first want to focus on our motivation for the project. Afterwards, we will briefly discuss the "state of the art". Next we will, as the name suggests, go into the design and a few key figures of the arm. In order for the arm to be properly controlled, we will also go into the forward and reverse kinematics. After that we will introduce you to our app and finally we will show a little demo of our arm.

## Slide 3: Motivation
Use in teaching
Material recycling
Easy start
in robotics
Notes: Since we are very interested in robotics, we wanted to develop our own arm. This arm can also be used later in teaching for illustrative purposes, or also for exercises in the robotics lectures. Furthermore, the arm offers a lighter and playful introduction to robotics. In addition, a positive side effect was that existing and disused hardware could be reused from the robotic lab

## Slide 4
Binning
Motion Model
Markov Localisation
GPS
Correlation
Mechanics
Sensor Model
Odometry
Probability
Sonar
Algorithms
Particlefilter
Orientation
Navigation
Resampling
OpenSLAM
LiDAR
Infrared
Radar
Position
Dead
reckoning
Occupancy Grid
Octomaps
Chamfer Matching
Least Mean Squares
Simulation
Classification
Autonomous
Position hypothesis
Tracking
Dynamics
Kalman-Filter
Coordinate transformations
Weighting
Ground Truth
Point Cloud
IMU
Kinematics
Pose Graph
Sensors
Estimation
ROS
Laser Scanner
Camera
Notes: Bzgl. „easy start in robotics“ -> Robotik enthält viele (komplizierte) Aspekte (einige sind auf der Folie genannt). Mit unserem Projekt geben wir nen Einblick in die typischen Aspekte, mit denen man oft in Berührung kommt (die farblich hervorgehobenen),  wiederum Vorteil für Lehre
------
Here are just a few things to do with robotics. Some of the first points you will encounter are the "Coordinate Transforamtions", "ROS", "Kinematics" and "Sensors". Our project provides a perfect start to these points.

## Slide 5: State of the Art
Notes: There is a wide selection of arms to buy. These go from very cheap to very expensive. There is also a wide range of arms in terms of angular resolution and repeatability. Meanwhile, there are also some DIY projects to find on the Internet.
As already stated in the motivation, however, we wanted to collect our own experiences and therefore decided to build our own arm.

## Slide 6: Construction
Repeatability of +/- 1°
~ 150 gr.
~ 200 gr.
Notes: For the people who are not in the first row, you can see here our finished prototype. This one offers 3 DOF, which you can see here. So that the arm can be fully controlled, 2 NXTs were installed. One of them can be seen here, the second one was placed below. In the current design and with the current translation, the arm can lift about 150g. Considering the weight of the arm of about 200g, the arm can lift about 75% of its own weight. However, it should be noted that this is only the weight of the arm. The base weighs much more, but the weight for the load capacity of the arm is irrelevant.
Furthermore, we found out after first tests that we have a repeatability of about 1 degree.

## Slide 7: Android Application
Christoph Ulrich, Benjamin Schaefer
7
Ubiquitous Computing Lab
Notes: Auf Achsenbedeutung eingehen!
The two diagrams show the repeated approach of the calibration position. The left image shows the lower joint, the right image the upper joint. After every 10 repetitions, the lower joint shows a repeatability of about 0.5 ° and the upper joint of 1 °. It should be noted, however, that at the lower joint a ratio of 1 to 42 was installed and in the upper joint only from 2 to 25.
However, this is only the theoretical approachability. Since the arm is made of Lego technology, the arm has some gear backlash. (wobble on the arm). The gear backlash has the biggest impact when the arm is orthogonal to the ground.
Now I would like to hand over to Christoph, who introduces you to the kinematics and the app.

## Slide 8: Forward Kinematics
Notes: To control the arm reliably -> forward and inverse kinematics.
Goal forward -> determine pose of tcp when a set of joint angles is given
Concatenation of n transformation matrices (coordinate systems), n -> number of joints
Tr matrix (DH) -> translation and rotation
Z rotation , translation parts -> x -> l * cos, y -> l * sin

## Slide 9: Inverse Kinematics
x
y
p
Law of Cosines

## Slide 10: Inverse Kinematics
Law of Cosines
x
y
p
Notes: Goal: calculate the set of joint angles when a tco pose is given
Just give idea about geometrical approach , not following every line

## Slide 11: Application - Architecture

## Slide 12: Android Application
Christoph Ulrich, Benjamin Schaefer
12

## Slide 13: Android Application
Christoph Ulrich, Benjamin Schaefer
13

## Slide 14: Application - Pipeline
onTouch Event
GUI
Inverse Kinematics
touchPoint(x,y)
ROS ActionClient
joint angles
ROS ActionServer
joint angles
ROS NXT Node
effort
Motors
power
update
Forward Kinematics
update
motor position

## Slide 15: Thanks for your attention. Questions?
Benjamin Schaefer, Christoph Ulrich
HTWG Konstanz Department of Computer Science
Ubiquitous Computing Lab
Alfred-Wachtel-Str. 8
D-78462 Konstanz (Germany)
Phone: +49 7531-206 0
URL: http://uc-lab.in.htwg-konstanz.de
Twitter: /UCLabHTWG
Facebook: /UCLabHTWG